Ausschreibungstext

Artikelnummer

203816

Typ

MC355-1T/1S

Kurzbeschreibung

Gigabit Ethernet Managed Medienkonverter, 1 Port, 1000TX auf 1000SX/LX/BX SFP

Hauptmerkmale

Gigabit Ethernet über SFP Mediakonverter

Ethernet 10/100/1000Base-TX

SFP separat zu bestellen

1 SFP Slot für individuelle Konfiguration

LED Anzeigen für Netzwerkdiagnose

Zeitsparende Plug&Play-Installation

Integriertes fernbedienbares Netzwerk-Management

Robustes, schmales IP30 Metallgehäuse

Betriebstemperatur -30º C ~ +75º C

Weitere Merkmale (Spezifikationen)

| Gerätetyp | Medienkonverter |
| --- | --- |
| Montage | DIN Rail, Wandmontage |
| Ports | 1x 10/100/1000Base-TX, 1x 1000Base-SX/LX/BX SFP |
| Bauart | Modul |
| Betriebsmodus | Single- / Multi Mode |
| Stromversorgung | 12~48VDC |
| Temperaturbereich (Betrieb) | -30º C ~ +75º C |
| Schutzart | IP30 |
| Hersteller-Nr. | MC355-1T/1S |

Zubehör

| MCR-R15 | Medienkonverter Rack, 15 Slots, 19", 2,4HU, 230VAC |
| --- | --- |
| S30-RJ | SFP Port Gigabit 2 Fiber Mini GBIC Modul,100m |
| S30-2MLC | SFP Mini-GBIC Transceiver, Multi Mode, 2 Fiber, 1000BASE-SX, 550m |
| S30-2MLC-2 | SFP Mini-GBIC Transceiver, Multi Mode, 2 Fiber, 1000Base-SX2, 2km |
| S30-1SLC/A-10 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX10-U, 10km |
| S30-1SLC/A-20 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX20-U, 20km |
| S30-1SLC/A-60 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX60-U, 60km |
| S30-1SLC/B-10 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX10-D, 10km |
| S30-1SLC/B-20 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX20-D, 20km |
| S30-1SLC/B-60 | SFP Mini-GBIC Transceiver, Single Mode, 1 Fiber, 1000Base-BX60-D, 60km |
| S30-2SLC-10 | SFP Mini-GBIC Transceiver, Single Mode, 2 Fiber, 1000Base-LX, 10km |