Ausschreibungstext

Artikelnummer

208136

Typ

AXIS P7216 VIDEO ENCODER

Kurzbeschreibung

Video Netzwerk Server, 16 Eingänge, H.264, 720x576, Audio

Hauptmerkmale

16-Kanal Video-Encoder

Simultane H.264 und MJPEG Streams

Hervorragende Videoqualität

Auflösung: 720x576 Pixel (D1)

Bildrate: 25 Bilder/Sek.

Hochauflösende Quad-Darstellung

Bidirektionale Audiofunktion

4x microSDHC Slot für lokale Speicher

Spannungsversorgung: 8-20VDC

Für Wand- und Rackmontage geeignet

ONVIF Konformität

Weitere Merkmale (Spezifikationen)

| Serie | Axis P72 |
| --- | --- |
| Bildauflösung max. | 720x576 |
| Bildübertragungsrate max. | 25 fps |
| Videoeingänge (Anzahl) | 16 |
| Kompressionsverfahren | H.264, M-JPEG |
| Alarmeingänge | 4 |
| Audiounterstützung | ja |
| Ethernet-Schnittstelle | 1000Base-T |
| Steuer-Schnittstellen | RS-485, RS-422 |
| Interner Speicher | microSD-Karte, microSDHC-Karte, microSDXC-Karte |
| Bauart | 19" Einschub |
| 19 Zoll einbaufähig | ja |
| Stromversorgung | 8-20VDC |
| ONVIF | ja |
| Hersteller-Nr. | 0542-002 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS MICROSDXC CARD 64GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS MICROSDXC CARD 64GB 10PCS | Speicherkarte, microSDXC, 64GB, 20 MB/s, inkl.SD-Adap., Axis zertifiziert, 10 Stück |
| AXIS T8310 CONTROL BOARD | Kontrollcenter, modular, mit Keypad, Joystick, Jog Dial |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS SURVEILLANCE CARD 64 GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS SURVEILLANCE CARD 128G | Speicherkarte, microSDXC, 128GB, Class 10, 30 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |