Ausschreibungstext

Artikelnummer

208466

Typ

AXIS Q7436

Kurzbeschreibung

Video Netzwerk Server, Einschubkarte, 6 Kanäle, 720x576, H.264, Coaxitron

Hauptmerkmale

6 Kanal Video Encoder Einschubkarte

Überrragende Bildverarbeitung

Multiple, individuel konfigurierbare H.264-/MJPEG-Ströme

Unterstützug von H.264 Base-, Main- und High-Profile

D1 Auflösung mit 60/50 fps pro Kanal

Integrierte Video Bewegungserkennung

Kompatibel mit Axis Camera Application Platform

Activer MAnipulationsalarm

Koax PTZ Control Unterstützung (Coaxitron)

Kompatibel mit AXIS Q7920/Q7900/291 1U

Weitere Merkmale (Spezifikationen)

| Serie | Axis Q74 |
| --- | --- |
| Bildauflösung max. | 720x576 |
| Bildübertragungsrate max. | 60 fps |
| Videoeingänge (Anzahl) | 6 |
| Kompressionsverfahren | M-JPEG, H.264 |
| Alarmeingänge | nein |
| Audiounterstützung | nein |
| Steuer-Schnittstellen | Coaxitron, RS-422, RS-485 |
| Interner Speicher | nein |
| Analysefunktionen | Bewegungserkennung (Motion Detection), Sabotageerkennung (Tampering) |
| Bauart | Karte |
| 19 Zoll einbaufähig | ja |
| Stromversorgung | 12VDC |
| ONVIF | ja |
| Hersteller-Nr. | 0584-001 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS Q7920 | Video Encoder Rack, 19"/5HE, 14 Hotswap Einschübe, RS-485, 4x SFP Slot, Aluminium |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS 291 VIDEO SERVER RACK | Video Server Einschub, 3 Steckplätze für Video Server-Karten, 100-240VAC |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |