Ausschreibungstext

Artikelnummer

212455

Typ

AXIS F4005 DOME SENSOR UNIT

Kurzbeschreibung

1/2,8? Dome Sensor Einheit, Einbau, 2,8mm, 1920x1200, für AXIS F41/F44

Hauptmerkmale

Dome Sensor Einheit für AXIS F41 und F44

Objektiv mit Festbrennweite 2.8 mm, F2.0

Bis 113° horizontaler Blickwinkel

HDTV 1080p mit AXIS F41, 720p mit AXIS F44

WDR Forensic Capture mit AXIS F41

Axis? Corridor Format Unterstützung

Für Innenbereich geeignet

Mit 12m Anschlusskabel zur Haupteinheit

Für Decken- und Wandeinbau

Einfache Installation

Weitere Merkmale (Spezifikationen)

| Serie | Axis F-Serie |
| --- | --- |
| Kameratyp | Kamera Sensoreinheit |
| Auflösungsstandard | HD 1080p |
| System | Farbe |
| Chipgröße | 1/2,8" |
| Aufnahmesensor | CMOS |
| Bildauflösung max. | 1920x1200 |
| Bildübertragungsrate max. | 25 fps |
| IR-Sperrfilter | Standard |
| Lichtempfindlichkeit | 0,3 Lux, bei F2,0 |
| Low Speed Shutter | ja |
| Wide Dynamic Range (WDR) | WDR Forensic Capture |
| Objektiv Typ | Festbrennweite |
| Brennweite | 2,8 mm |
| Blendensteuerung | nein |
| Digital Zoom | nein |
| Bildwinkel horizontal | 113 ° |
| Beleuchtung | nein |
| Gehäuse | Innen |
| Farbe (Gehäuse) | weiß |
| Farbe (Kuppel) | klar |
| Gehäusematerial | Kunststoff |
| Heizung | nein |
| Scheibenheizung | nein |
| Lüfter | nein |
| Videoausgänge | nein |
| Alarmeingänge | nein |
| Alarmausgänge | nein |
| Audiounterstützung | nein |
| Ethernet-Schnittstelle | 100Base-TX |
| Steuer-Schnittstellen | nein |
| Interner Speicher | nein |
| Montageart | Deckeneinbau |
| Temperaturbereich (Betrieb) | -30°C ~ +55°C |
| Schutzart | keine Angabe |
| Hersteller-Nr. | 0798-001 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |