Ausschreibungstext

Artikelnummer

221065

Typ

AXIS P9106-V BRUSHED STEEL

Kurzbeschreibung

1/3" Netzwerk Dome, Farbe, 2016x1512, 1,8mm, Eckgehäuse, Edelstahl, IP66, IK10

Hauptmerkmale

Eckgehäuse ohne offen liegende Verankerungspunkte

Frontscheibe abrieb- und chemikalienresistent

AXIS T61 Portcast Serie wird unterstützt

Optimiertes Sichtfeld: 130° HFoV 95° VFoV

Objektiv mit Festbrennweite: F2,4/1,8mm

Empfindlichkeit: 0,35Lux (50 IRE, F2,4)

Auflösung: 2016 x 1512 @ 25fps im 4:3 Format

Vandalismusgeschützt nach IK10

Wasser- und Staubdicht nach IP66

Für Innen, Temperaturbereich -15°C - 50°C

Robustes Edelstahl-Gehäuse

Weitere Merkmale (Spezifikationen)

| Serie | Axis P91 |
| --- | --- |
| Kameratyp | Eckgehäuse |
| Auflösungsstandard | 3 Megapixel |
| System | Farbe |
| Chipgröße | 1/3" |
| Aufnahmesensor | CMOS |
| Videokompression | H.264, M-JPEG |
| Bildauflösung max. | 2016x1512 |
| Bildübertragungsrate max. | 25 fps |
| IR-Sperrfilter | Standard |
| Lichtempfindlichkeit | 0,35 Lux, bei F2,4, 50 IRE |
| Low Speed Shutter | nein |
| Wide Dynamic Range (WDR) | WDR |
| Bewegungsmelder | ja |
| Objektiv Typ | Festbrennweite |
| Brennweite | 1,8 mm |
| Blendensteuerung | nein |
| Digital Zoom | ja |
| Bildwinkel horizontal | 130 ° |
| Beleuchtung | nein |
| Gehäuse | Innen |
| Farbe (Gehäuse) | Edelstahl |
| Gehäusematerial | Edelstahl |
| Scheibenheizung | nein |
| Videoausgänge | nein |
| Alarmeingänge | nein |
| Audiounterstützung | nein |
| Interner Speicher | microSD-Karte, microSDHC-Karte, microSDXC-Karte |
| Stromversorgung | PoE |
| Power over Ethernet | IEEE 802.3af |
| Vandalismusgeschützt | ja |
| Temperaturbereich (Betrieb) | -15°C ~ +50C° |
| Schutzart | IP66 |
| ONVIF | ja |
| Zertifizierungen | IK10 |
| Hersteller-Nr. | 01553-001 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T81B22 DC 30W MIDSPAN | PoE+ Midspan, IEEE802.3at, 12/24V Eingang, -20°C bis 65°C |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| NETWORK CABLE COUPLER IP66 | RJ45 Koppler, Buchse-Buchse, für Außen, IP66 |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS T8120 15W MIDSPAN 1-PORT | PoE Midspan, 1 Port, IEEE802.3af, 10/100Mbps |
| AXIS T8123-E OUTDOOR MIDSPAN 3 | PoE Midspan, 1 Port, IEEE802.3at, 30W, IP66, -40°C - +55°C |
| AXIS T8124-E OUTDOOR MIDSPAN 6 | PoE Midspan, 1 Port, IEEE802.3at, 60W, IP66, -40°C - +55°C |
| NETWORK CABLE COUPLER INDOOR | RJ45 Koppler, Buchse-Buchse, nur für Innenraum |
| NETWORK CABLE COUPLER INDOOR S | RJ45 Koppler, Buchse-Buchse, nur für Innenraum, kompakte Ausführung |
| AXIS T8125 AC 24V Midspan 60W | High PoE Midspan, 1 Port, 60W, Gigabit, -10 - +65°C, 24V AC IEEE802.3at, IEEE802.3af |
| AXIS T8133 30W MIDSPAN | PoE+ Midspan, IEEE802.3at, Type 2, Class 4, 1 Port |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS T8134 60W MIDSPAN | High PoE Midspan, 1 Port, 60W, Gigabit, -10 - +45°C, 100-240V IEEE802.3at, IEEE802.3af |
| AXIS T8415 INSTALLATION TOOL | Installations Tool, zur Axis Kamera Einrichtung, WLAN, Akku, USB, PoE+, ONVIF |
| AXIS POE MIDSPAN 16-PORT | PoE Midspan, 16 Port, IEEE802.3af, 90-264VAC |
| AXIS POE MIDSPAN 8-PORT | PoE Midspan, 8 Port, IEEE802.3af, 90-264VAC |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS SURVEILLANCE CARD 64 GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS T8516 POE+ NETWORK SWITCH | Gigabit Switch, managed, 16 PoE+ Ports, 2x SFP/RJ45 Uplinks, 240W PoE, 19", 1HE |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |
| AXIS T8606 MEDIA CONV SWITCH 2 | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP, 24VDC |
| AXIS T8154 60W SFP MIDSPAN | PoE Midspan, 1 Port, 60W, SFP-Slot, Gigabit, 100-240V |
| AXIS T8144 60W INDUSTRIAL MIDS | High PoE Midspan, 1 Port, 60W, Gigabit, -40 - +75°C, 20-60VDC DIN Montage |
| AXIS T8508 POE+ NETWORK SWITCH | Gigabit Switch, managed, 8 PoE+ Ports, 2x SFP/RJ45 Uplinks, 130W PoE, 1HE |
| AXIS T8524 POE+ NETWORK SWITCH | Gigabit Switch, managed, 24 PoE+ Ports, 2x SFP/RJ45 Uplinks, 370W PoE, 19", 1HE |
| AXIS T8504-E OUTDOOR POE SWITC | Gigabit Switch, managed, 4 PoE+ Ports bis 60W, SFP Uplink, 150W PoE, Außen, IP67 |
| AXIS T90D25 W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, 12-24V, 24W, IP66, IK9 |
| AXIS T90D25 POE W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, PoE, 25W, IP66, IK09 |
| AXIS T90D35 W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, 12-24V, 42W, IP66, IK9 |
| AXIS T90D35 POE W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, PoE, 47W, IP66, IK09 |
| AXIS SURVEILLANCE CARD 128 GB | Speicherkarte, microSDXC, 128GB, Class 10, 50-80 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS T8645 POE+ COAX COMPACT K | PoE+ über Coax Set, 1x AXIS T8641 Base Einheit, 1x AXIS T8643 Device Einheit |
| AXIS T8648 POE+ COAX BLADE COM | PoE+ über Coax Set, 1x AXIS T8646 Einschubkarte, 6x AXIS T8643 Device Einheiten |
| AXIS T6101 AUDIO AND I/O INTER | Netzwerk I/O Audio Modul, 2-Wege-Audio, überwachte Ein-/Ausgänge, PoE |
| AXIS T6112 AUDIO AND I/O INTER | Netzwerk I/O Audio Modul, 2-Wege-Audio, Mikrofon, überwachte Ein-/Ausgänge, PoE |
| AXIS T8129-E OUTDOOR POE EXTEN | PoE Extender, PoE, PoE+, Außen, IP66/67, 200m Reichweite |
| AXIS SURV MICRO SDXC CARD 256G | Speicherkarte, microSDXC, 256GB, Class 10, V30, inkl. SD-Adapter, Axis zertifiziert |
| AXIS P91 SKIN COVER A BRUSHED | Gehäuseabdeckung, lackierbar, Edelstahl, für AXIS P91 Serie, Magnethalterung |