Ausschreibungstext

Artikelnummer

98722

Typ

AXIS P7701 BAREBOARD

Kurzbeschreibung

Netzwerk Video Decoder, 1-Kanal, H.264, MPEG-4, PoE, ohne Netzteil/Gehäuse

Hauptmerkmale

1-Kanal Netzwerk-Videodecoder

Bareboard Version ohne Gehäuse

Dekomprimierung von H.264, MPEG-4 und MJPEG

Decodierung mit voller Bildrate möglich

Digitale oder analoge Videoausgabe

Automatische Anzeige alarmgesteuerter Aufnahmen

Decodiert auch Mono-Audio

Ausgezeichnete Audio-Qualität

Stromversorgung über PoE oder externes Netzteil

Lieferung ohne Netzgerät/Gehäuse

Weitere Merkmale (Spezifikationen)

| Serie | Axis P77 |
| --- | --- |
| Bildauflösung max. | 1280x720 |
| Bildübertragungsrate max. | 25 fps |
| Kanäle gesamt | 1 |
| Kompressionsverfahren | H.264, M-JPEG, MPEG-4 |
| Alarmausgang | ja |
| Audiounterstützung | ja |
| Ethernet-Schnittstelle | 100Base-TX, 10Base-T |
| Steuer-Schnittstellen | RS-485, RS-422 |
| Bauart | Karte |
| Stromversorgung | 8-20VDC, PoE |
| Leistungsaufnahme | 8,3W |
| Temperaturbereich (Betrieb) | 0°C ~ +50°C |
| ONVIF | nein |
| Hersteller-Nr. | 0319-041 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS P7701 EXT.WARRANTY | Erweiterung der Gewährleistung für AXIS P7701 um 2 Jahre, max. 5 Jahre insg. |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |