Ausschreibungstext

Artikelnummer

220808

Typ

AXIS S1116 RACKED

Kurzbeschreibung

Netzwerk Video Rekorder, 16 IP Kanäle (max. 32), 3x SATA, 1x 8TB HDD, Rackeinbaugehäuse

Hauptmerkmale

Vorinstallierter Axis Camera Station Rekorder

16 AXIS Camera Station 5.x Core Lizenzen

Erweiterung auf max. 32 Kanäle möglich

256 Mbit/s Gesamtdatendurchsatz (Aufnahme)

Intel® i5-8500, 6x 3.0 GHz, 8GB RAM

1x 8TB Enterprise HDD, 7200 rpm, SATA 6Gb/s

Insgesamt drei HDD Steckplätze für Speicher

Verwendung von Cient-PC für Liveansicht empfohlen

Microsoft Windows 10 Enterprise auf 128 GB SSD

2x USB 3.1, 1x USB 3.1 Type C, 2x Display Port 1.2

Rackeinbaugehäuse, 19", 1 HE

Onsite Hardware Replacement Service

Weitere Merkmale (Spezifikationen)

| Serie | Axis S11 |
| --- | --- |
| IP Kanäle | 16 |
| Auflösung Aufzeichnung max. | keine Angabe |
| Kompressionsverfahren | H.265, H.264, M-JPEG |
| Monitor-Ausgänge | 2x DisplayPort |
| Netzwerk | 1x 100/1000Base-TX RJ45, 1x 10GBASE-T RJ45 |
| Audiounterstützung | ja |
| Festplattenkapazität (max. intern) | 24 TB |
| Festplattenkapazität (intern) | 8 TB |
| Schnittstellen externer Speicher | USB |
| Anzahl HDD Steckplätze | 3x SATA |
| HDD Hotswap | keine Angabe |
| USB Ports | 2x USB 3.1, 1x USB 3.1 Type-C |
| RAID | nein |
| Datendurchsatz maximal | 256 Mbps |
| ONVIF | ja |
| Hersteller-Nr. | 01618-001 |

Zubehör

| AXIS A1001 | Netzwerk Tür Controller, 2x Tür, 2x Leser, 2x AUX, Wiegand, RS-485, OSDP, PoE |
| --- | --- |
| AXIS P8221 | Netzwerk I/O Audio Modul, Vorverstärker, 8 Ein-/Ausgänge, Netzgerät |
| AXIS T8311 JOYSTICK | 3-Achsen Joystick, für Axis PTZ Kameras, Domes |
| AXIS T8312 KEYPAD | Keypad, Tastatur für Axis PTZ Kameras, Domes |
| AXIS T8310 CONTROL BOARD | Kontrollcenter, modular, mit Keypad, Joystick, Jog Dial |
| AXIS T8313 JOG DIAL | Jog Shuttle für Axis PTZ Kameras und Domes |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS S9002 | Desktop Terminal PC, Axis Camera Station Client, Quad Monitor, max. 3x 4K-Streams |
| AXIS S9001 MKII | Desktop Terminal PC, Axis Camera Station Client, Dual Monitor, max. 1x 4K-Stream |
| AXIS T8516 POE+ NETWORK SWITCH | Gigabit Switch, managed, 16 PoE+ Ports, 2x SFP/RJ45 Uplinks, 240W PoE, 19", 1HE |
| AXIS S9101 | Desktop Terminal PC, Axis Camera Station Client, Dual Monitor, DisplayPort, HDMI |
| AXIS T8508 POE+ NETWORK SWITCH | Gigabit Switch, managed, 8 PoE+ Ports, 2x SFP/RJ45 Uplinks, 130W PoE, 1HE |
| AXIS T8524 POE+ NETWORK SWITCH | Gigabit Switch, managed, 24 PoE+ Ports, 2x SFP/RJ45 Uplinks, 370W PoE, 19", 1HE |
| AXIS T8504-E OUTDOOR POE SWITC | Gigabit Switch, managed, 4 PoE+ Ports bis 60W, SFP Uplink, 150W PoE, Außen, IP67 |
| AXIS A1601 | Netzwerk Tür Controller, 2x Tür, 2x Leser, 2x AUX, 2x Relais, RS-485, OSDP, PoE+ |
| AXIS T8504-R INDUSTRIAL POE SW | Gigabit Switch, managed, 4 PoE+ Ports bis 60W, SFP Uplink, 240W PoE Budget |
| AXIS S9201 MKII | Desktop Terminal PC, Axis Camera Station Client, All In One, 22" Monitor, Maus, Keyb. |
| AXIS S9002 MK II | Desktop Terminal PC, Axis Camera Station Client, für vier Monitore bis 4K@25fps |